## Slide 1
Reliability Centered Maintenance (RCM)
A Case Study for FMEA, Criticality, and Task Selection
Nancy Regan
RCM Practitioner

## Slide 2
Case Study
2014 Subaru Forester Low Engine Oil Light
2 hours from home

## Slide 3: Workshop Agenda
Goal: Understand SAE-JA1011 Compliant RCM
  Real-World (personal!) Case Study
    Build an FMEA for 4 Failure Modes (scope!)
    Assess Consequences
    Use RCM Logic to establish a CBM task
  NOT a comprehensive introduction to RCM. It is an overview of some key RCM concepts.
  You WILL leave understanding what “True” RCM is.

## Slide 4
Reliability Centered Maintenance (RCM) Overview

## Slide 5
Case Study
2014 Subaru Forester Low Engine Oil Light
2 hours from home
Operating Context Excerpt
2014 Subaru Forester – personal use vehicle. (I drive it almost exclusively.)
Drive approximately 12,000 miles per year in the Southeastern United States (almost entirely in Alabama). Longest journey ~ 4 hours from home.
I do have a “backup” car – 2004 Toyota Corolla.
Scope of analysis is limited to Failure Modes that result in illumination of the Low Engine Oil Light and the “Low Engine Oil Light system” itself.
2.5-liter horizontally opposed four-cylinder (boxer) engine, 170 horsepower.
Low Engine Oil Light illuminates in the event that the engine oil decreases to the lower limit (2 quarts low).

## Slide 6
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
Reliability Centered Maintenance

## Slide 7
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
“Reliability”
Reliability Centered Maintenance
Include Primary & Secondary Functions

## Slide 8
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
To get from “Point A” to “Point B.”
X

## Slide 9
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Go up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 10
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Go up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 11
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Go up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 12
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Go up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 13
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Drive up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 14
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Drive up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 15
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Drive up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required

## Slide 16
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Drive up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.

## Slide 17
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.

## Slide 18
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Continue listing Secondary Functions.
2
3
4
… And so on

## Slide 19
Evident and Hidden Functions

## Slide 20
Classifying Functions: Evident
Evident Function
Failure of the Function becomes evident to the operating crew under normal conditions.

## Slide 21
Primary Function: My 2014 Subaru Forester
Verb
+
Performance Standard(s)
+
Operating Context
To
+
Object
+
Verb | Transport
Object | Up to 5 adult passengers and 3 medium-size suitcases
Performance Standards | Along paved roads and highways Go up to 360 miles without stopping In climates that range from 0º to 115º F (-17º to 46º C) While protecting passengers from the elements
Operating Context | As required
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Evident
Function

## Slide 22
Classifying Functions: Hidden
Hidden Function
Failure of the Function is not evident to the operating crew under normal conditions.
Hidden Functions are almost always Protective Devices

## Slide 23: Protective Devices and Hidden Failures
Protective Device:
Device or System intended to protect in the event that another failure occurs.
Notes: It was born out of extraordinary circumstance.

## Slide 24
Hidden Functions
Home Smoke Detector
Sound an audible alarm in the event there is a fire in the room
Protective Device
Hidden Function
Failure of the Function is not evident to the operating crew under normal conditions.
No fire
(normal condition)
+
Smoke detector fails

## Slide 25
Hidden Functions
Home Smoke Detector
Sound an audible alarm in the event there is a fire in the room
Protective Device
There IS a fire in the room
(failure condition)
+
Smoke detector fails
=
Multiple Failure

## Slide 26
Case Study
2014 Subaru Forester Low Engine Oil Light
What is the Function?
  To be capable of visually alerting the driver in the event that the engine oil level decreases to the low level limit. (LOW OIL LEVEL Light)

## Slide 27
Case Study
2014 Subaru Forester Low Engine Oil Light
What is the Multiple Failure?
  Oil in the reservoir falls to the low level limit
  Low Engine Oil Light “system” is failed.

## Slide 28
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower level limit. (LOW OIL LEVEL Light)
Hidden
Function
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit (LOW OIL LEVEL Light)
Failure Modes and Effects Analysis (FMEA)
Is this an Evident or Hidden Function?

## Slide 29
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
Reliability Centered Maintenance
Total Failure
Partial Failure

## Slide 30
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
What is Total Failure?

## Slide 31
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Completely unable to transport.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Total Failure

## Slide 32
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower level limit. (LOW OIL LEVEL Light)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit (LOW OIL LEVEL Light)
Failure Modes and Effects Analysis (FMEA)
What is Total Failure?

## Slide 33
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower level limit. (LOW OIL LEVEL Light)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit (LOW OIL LEVEL Light)
Failure Modes and Effects Analysis (FMEA)
Incapable of visually alerting the driver in the event that the engine oil level decreases to the lower limit.
Total Failure

## Slide 34
Failure Modes and Effects Analysis (FMEA)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower level limit. (LOW OIL LEVEL Light)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit (LOW OIL LEVEL Light)
How else can it fail?

## Slide 35
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit (LOW OIL LEVEL Light)
Failure Modes and Effects Analysis (FMEA)
Falsely illuminates the LOW OIL LEVEL Light.
Falsely illuminates the LOW OIL LEVEL Light.

## Slide 36
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
We manage assets at the Failure Mode level.
We proactively identify what could cause each Functional Failure, and then use the remaining four steps of the RCM process to figure out what (if anything at all) we should do to manage it.
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
What specifically causes failure
Reliability Centered Maintenance

## Slide 37
Failure Mode
Destination:
Failure Management Strategies
Proactive Maintenance
and
Default Strategies
A properly written Failure Mode puts you on the right road and sends you in the right direction.
Failure Modes

## Slide 38
Proactive Maintenance Plan
New/Modifications to Operating Procedures
Failure Finding tasks
Updates/Additions to Technical Publications
New/Modifications to Training Programs
Equipment Redesigns
Troubleshooting Procedures
Supply Changes
RCM Can Yield
Potential Products of an RCM Analysis

## Slide 39
How to Compose Failure Modes
Noun
+
(as necessary) Operating Context
Verb
+
Intercooler tubes corrode
Brake pads wear
Compressor disc fatigues
Alternator belt deteriorates
Power turbine blade fatigues

## Slide 40
How to Compose Failure Modes
Noun
+
(as necessary) Operating Context
Verb
+
Intercooler tubes corrode
Brake pads wear
Compressor disc fatigues
Alternator belt deteriorates
Power turbine blade fatigues
due to normal use
due to normal use
due to normal use
due to normal use
due to normal use

## Slide 41
How to Compose Failure Modes
Noun
+
(as necessary) Operating Context
Verb
+
Hydraulic line chafes
Hydraulic line chafes
due to normal equipment vibration
due to improper routing
Oil filter clogs
Oil filter clogs
due to normal use
due to gearbox break-in
Foreign object enters aircraft engine air inlet
Foreign objects accumulate in aircraft engine inlet
during flight
while on the ground,
with engine off

## Slide 42
Why Including Operating Context in Failure Modes Matters
Failure Mode
Destination:
Failure Management Strategies
Proactive Maintenance
and
Default Strategies

## Slide 43
Why Operating Context Matters in Failure Modes
Hydraulic line chafes due to normal equipment vibration.
Failure Modes with operating context in italics
Hydraulic line chafes due to improper routing.
Visually inspect hydraulic line every 25 hours of operation.
Failure Management Strategies
Augment training program so that hydraulic lines are routed properly.

## Slide 44
Why Operating Context Matters in Failure Modes
Hydraulic line chafes due to normal equipment vibration.
Oil filter clogs due to normal use
Failure Modes with operating context in italics
Oil filter clogs due to gearbox break-in
Hydraulic line chafes due to improper routing.
Visually inspect hydraulic line every 25 hours of operation.
Failure Management Strategies
Augment training program so that hydraulic lines are routed properly.
Change the oil filter after every 500 hours of operation.
Change the oil filter after the first 50 hours of operation.

## Slide 45
Why Operating Context Matters in Failure Modes
Hydraulic line chafes due to normal equipment vibration.
Oil filter clogs due to normal use
Foreign object enters engine air inlet during flight.
Foreign object accumulates in engine inlet while aircraft is on the ground with the engine not running.
Failure Modes with operating context in italics
Oil filter clogs due to gearbox break-in
Hydraulic line chafes due to improper routing.
Visually inspect hydraulic line every 25 hours of operation.
Failure Management Strategies
Augment training program so that hydraulic lines are routed properly.
Change the oil filter after every 500 hours of operation.
Change the oil filter after the first 50 hours of operation.
Formulate emergency procedure for an in-flight engine failure.
Inspect the engine inlet for foreign objects prior to engine start.

## Slide 46
Why Operating Context Matters in Failure Modes
Hydraulic line chafes due to normal equipment vibration.
Failure Modes with operating context in italics
Hydraulic line chafes due to improper routing.
Visually inspect hydraulic line every 25 hours of operation. Replace, as required.
Failure Management Strategies
Augment training program so that hydraulic lines are routed properly.

## Slide 47
Case Study
2014 Subaru Forester Low Engine Oil Light
2 hours from home
What specifically could cause (Failure Modes) the engine oil to drop to the low level limit and illuminate the LOW OIL LEVEL Light?

## Slide 48
What specifically could cause the engine oil to drop to the low level limit and illuminate the LOW OIL LEVEL LIGHT?
1
2
3
The light could illuminate because the oil level is low due to “normal consumption.” In that case, I had enough oil to make it home without damaging my engine because I only had another 150 miles to go. But, it wouldn’t be wise to continue driving without checking the oil level to ensure I avoid any possible engine damage.
The light could illuminate because the oil level was low due to a leak in the oil system. That’s the worst-case-scenario. Low oil level leads to inadequate lubrication which could cause serious internal damage to engine components and possibly leave me stranded on the side of the road.
The light could falsely illuminate due to a faulty circuit (meaning the engine oil level is normal but the light illuminates anyway). If that is the case, there is nothing I can do about it until I bring my car in for service. But between now and then, my engine will be just fine (assuming I don’t also have a low oil situation in the meantime!)
Failure Modes
Failure Effects
Failure Consequences
Failure Management Strategies

## Slide 49
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
Failure Effect
A story of what would happen if nothing were done to predict, prevent, or manage its associated Failure Mode.
Reliability Centered Maintenance
Important Points
Document worst-case-scenario
Write in enough detail to assess consequences

## Slide 50
Failure Effects Include:
  A description of the failure process from the occurrence of the Failure Mode to the Functional Failure
  Physical evidence that the failure has occurred
  How it adversely affects safety and/or the environment
  How it affects operational capability/mission
  Specific operating restrictions as a result of the failure
  Secondary damage
  What must be done and how long it takes to repair the failure

## Slide 51
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
1. Engine consumes oil due to normal use.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.

## Slide 52
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
During engine operation, the oil is gradually consumed by the engine. The decrease in oil is indicated on the dipstick. If this goes unnoticed, eventually the engine oil drops to the point that the LOW OIL LEVEL Light illuminates. The driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil is low. The driver replenishes the oil and continues to the destination but with some delay. Downtime to repair, up to 30 minutes.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Engine consumes oil due to normal use.
Note: The Failure Mode is recorded under “Total Failure” because the light “imposes operating restrictions as a result of the failure.”

## Slide 53
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)

## Slide 54
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)
Incapable of visually alerting the driver in the event that the engine oil level decreases to the lower limit.
?
What specifically causes…?

## Slide 55
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)
Incapable of visually alerting the driver in the event that the engine oil level decreases to the lower limit.
LOW OIL LEVEL Light circuit fails open.

## Slide 56
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
LOW OIL LEVEL LIGHT circuit fails open.
This Failure Mode only matters in the event that the engine oil level decreases to the lower limit. The driver is unaware of the low oil situation and continues to operate the vehicle. The oil level continues to drop. Engine components are not properly lubricated and start to wear abnormally. Eventually, engine oil pressure decreases and engine oil temperature increases. The OIL PRESSURE warning light and/or the CHECK ENGINE light illuminates on the dashboard. Driver must pull over and cannot get to the desired destination on time. It is likely driver can find a safe place to pull over and call a tow truck. However, worst case, driver must pull over on a busy highway or on a dark country road at night. The oil system is repaired, as required. Any secondary engine damage is repaired, as required. Worst case, engine must be replaced. Downtime to repair, 3 days to 1 month at a cost ranging from $1,000 to $8,000.

## Slide 57
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
Safety
Environmental
Operational
Non-Operational
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
Reliability Centered Maintenance

## Slide 58
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
Proactive Maintenance
Scheduled Restoration
Scheduled Discard
Condition Based Maintenance
Also known as:
On-Condition Maintenance
Predictive Maintenance (PdM)
Figure out how to manage each Failure Mode
Reliability Centered Maintenance

## Slide 59
RCM Decision Diagram

## Slide 60
RCM Decision Diagram
EVIDENT SIDE
HIDDEN SIDE
Without inspection, will the loss of Function caused by this Failure Mode become Evident during normal situations?
Safety
Environ- mental
Operational
Non- Operational
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
YES
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
NO
NO
NO
Safety
Environ- mental
Operational
Non- Operational
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
NO
NO
NO
NO
YES
YES
YES
YES
YES
YES
YES
YES

## Slide 61
RCM Decision Diagram
EVIDENT SIDE
HIDDEN SIDE
Without inspection, will the loss of Function caused by this Failure Mode become Evident during normal situations?
YES
NO

## Slide 62
RCM Decision Diagram
EVIDENT SIDE
HIDDEN SIDE
Without inspection, will the loss of Function caused by this Failure Mode become Evident during normal situations?
Safety
Environ- mental
Operational
Non- Operational
YES
NO
NO
NO
Safety
Environ- mental
Operational
Non- Operational
NO
NO
NO
NO
YES
YES
YES
YES
YES
YES
YES
YES
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
Safety
Environmental
Operational
Non-Operational

## Slide 63
RCM Decision Diagram
EVIDENT SIDE
HIDDEN SIDE
Without inspection, will the loss of Function caused by this Failure Mode become Evident during normal situations?
Safety
Environ- mental
Operational
Non- Operational
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
YES
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
NO
NO
NO
Safety
Environ- mental
Operational
Non- Operational
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
NO
NO
NO
NO
YES
YES
YES
YES
YES
YES
YES
YES

## Slide 64
RCM Decision Diagram
Without inspection, will the loss of Function caused by this Failure Mode become Evident during normal situations?
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
YES
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy!
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
CBM
Restoration
Replacement
Assign
Default Strategy?
DS?
Yes
No
Yes
Yes
Assign
DS?
Assign
DS?
No
No
YES
YES
YES
YES
YES
YES
YES
YES
EVIDENT SIDE
HIDDEN SIDE
Safety
Environ- mental
Operational
Non- Operational
NO
NO
NO
Safety
Environ- mental
Operational
Non- Operational
NO
NO
NO
Proactive Tasks Must be Technically Feasible AND Worth Doing in order to assign them.

## Slide 65
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Falsely illuminates the LOW OIL LEVEL Light.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Apply the RCM Decision Diagram

## Slide 66
  An On-Condition task is performed at a defined interval to detect a Potential Failure Condition so that maintenance can be performed before the failure occurs.
On-Condition Maintenance

## Slide 67
How can a Potential Failure Condition be detected?
Using relatively simple techniques such as monitoring gauges, measuring brake linings, or feeling for vibration via Human Senses
Employing more technically involved techniques such as thermography, frequency analysis, oil analysis, or thermal imaging
Continuous monitoring with devices installed directly on machinery (e.g. strain gauge, accelerometer, etc.)
On-Condition Maintenance

## Slide 68
Two Criteria to assign a Proactive Maintenance Task
In the context of RCM, in order to assign a
Proactive Maintenance task, two criteria must be satisfied:
1. Technically Appropriate
AND
2. Worth Doing
With respect to an On-Condition task, let’s start with what makes it technically feasible.

## Slide 69
Condition Based Maintenance (CBM)
In order to determine if an On-Condition task is technically appropriate, Potential Failure Conditions must be evaluated.

## Slide 70
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve

## Slide 71
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve
F: Failure



P: Potential Failure Condition:
New component Installed
P-F Interval

## Slide 72
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
Belt breaks
P-F Interval

## Slide 73
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
6 months
Belt breaks

## Slide 74
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
6 months
Belt breaks
Belt is inspected just before visual evidence of wear is visually detectable

## Slide 75
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
6 months
Belt breaks
Belt is inspected just before visual evidence of wear is visually detectable

The visual evidence of wear is detected on the next inspection, 3 months later
Minimum time remaining to do something about it…to take action to manage the consequences of failure…
3 months
POINT: It doesn’t matter how often the failure occurs. What matters is how quickly failure occurs once the Potential Failure Condition is detectable.

## Slide 76
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
6 months
Belt breaks
Belt is inspected just before visual evidence of wear is visually detectable

The visual evidence of wear is detected on the next inspection, 3 months later
Minimum time remaining to do something about it…to take action to manage the consequences of failure…
3 months
Scenario 1: Asset taken offline yearly. Can it be monitored at intervals less than the P-F Interval?

## Slide 77
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Visual evidence of cuts and frays
New V-Belt Installed
6 months
Belt breaks
Belt is inspected just before visual evidence of wear is visually detectable

The visual evidence of wear is detected on the next inspection, 3 months later
Minimum time remaining to do something about it…to take action to manage the consequences of failure…
3 months
Scenario 2: Asset taken offline every month. Can it be monitored at intervals less than the P-F Interval?
Shutdown Schedules…

## Slide 78
Resistance to Failure
Time
Condition Based Maintenance (CBM)
P-F Curve



F: Failure
P: Potential Failure Condition:
Brake pads worn to only 1/16” remaining
Brake Pads Installed
1 Year
Brake drums damaged

## Slide 79
The manner in which On-Condition task intervals are set is a widely misunderstood concept.
  Four Key Points:
  On-Condition maintenance task intervals are NOT based upon MTBF.
  On-Condition maintenance task intervals are NOT based upon the useful life of a component.
  On-Condition maintenance task intervals are NOT based upon the criticality of the failure.
  On-Condition maintenance task intervals are based upon…

## Slide 80
Resistance to Failure
Time
F: Functional Failure



P: Potential Failure Condition
New component Installed
P-F Interval
Condition Based Maintenance (CBM)
P-F Curve
How QUICKLY failure occurs once the Potential Failure Condition is detectable.
Achieve maximum useful life of components

## Slide 81
Failure Effect
During engine operation, the oil is gradually consumed by the engine. The decrease in oil is indicated on the dipstick. If this goes unnoticed, eventually the engine oil drops to the point that the LOW OIL LEVEL Light illuminates (down 2 quarts). The driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil is low. The driver replenishes the oil and continues to the destination but with some delay. Downtime to repair, up to 30 minutes.
Failure Mode
Engine consumes oil due to normal use.
Apply the RCM Decision Diagram

## Slide 82
Failure Effect
During engine operation, the oil is gradually consumed by the engine. The decrease in oil is indicated on the dipstick. If this goes unnoticed, eventually the engine oil drops to the point that the LOW OIL LEVEL Light illuminates (down 2 quarts). The driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil is low. The driver replenishes the oil and continues to the destination but with some delay. Downtime to repair, up to 30 minutes.
Failure Mode
Engine consumes oil due to normal use.
Apply the RCM Decision Diagram

## Slide 83
Failure Effect
During engine operation, the oil is gradually consumed by the engine. The decrease in oil is indicated on the dipstick. If this goes unnoticed, eventually the engine oil drops to the point that the LOW OIL LEVEL Light illuminates (down 2 quarts). The driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil is low. The driver replenishes the oil and continues to the destination but with some delay. Downtime to repair, up to 30 minutes.
Failure Mode
Engine consumes oil due to normal use.
Apply the RCM Decision Diagram

## Slide 84
Resistance to Failure
Time
Failure



Potential Failure Condition
Oil is Replaced
P-F Interval
P-F Curve
Failure Mode
Engine consumes oil due to normal use.

## Slide 85
Resistance to Failure
Time
Failure



Potential Failure Condition
Oil is Replaced
P-F Interval
P-F Curve
Failure Mode
Engine consumes oil due to normal use.
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 86
Resistance to Failure
Time
Failure



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
Failure Mode
Engine consumes oil due to normal use.
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 87
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
F: Oil level drops to the “low level”
P: Oil level is 75% to the “low level”
Failure Mode
Engine consumes oil due to normal use.
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 88
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
Failure Mode
Engine consumes oil due to normal use.
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 89
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
<1200 Miles
Failure Mode
Engine consumes oil due to normal use.
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 90
300 miles
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
300 miles
300 miles
300 miles
Failure Mode
Engine consumes oil due to normal use.
<1200 Miles
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 91
300 miles
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
300 miles
300 miles
300 miles
900 miles
Failure Mode
Engine consumes oil due to normal use.
<1200 Miles
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 92
300 miles
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
300 miles
300 miles
300 miles
900 miles
Failure Mode
Engine consumes oil due to normal use.
<1200 Miles
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 93
300 miles
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
300 miles
300 miles
300 miles
900 miles
How far can I go on one tank of fuel?
16 gallons of fuel x 30 mpg = 480 miles
Failure Mode
Engine consumes oil due to normal use.
<1200 Miles
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 94
300 miles
Resistance to Failure
Time



Oil is Replaced
P-F Interval
P-F Curve
P: Oil level is 75% to the “low level”
F: Oil level drops to the “low level”
According to my Subaru Forester manual
Subaru manual states that “consuming more than 1 quart per 1,200 miles” is abnormal.
They recommend checking the engine oil level at each fuel stop.
300 miles
300 miles
300 miles
900 miles
How far can I go on one tank of fuel?
16 gallons of fuel x 30 mpg = 480 miles
If I check the oil every time I stop for gas, that would be about every 400 miles and that IS practical.
Failure Mode
Engine consumes oil due to normal use.
<1200 Miles
Copyright The Force, Inc. 2023 All Rights Reserved

## Slide 95
Failure Mode
Engine consumes oil due to normal use.
Apply the RCM Decision Diagram
Must answer “YES” to ALL questions to assign a task.
Task:
At every fuel stop, check the engine oil level using the dipstick. Replenish the reservoir, as required.

## Slide 96
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
RCM is a zero-based process used to identify the Failure Management Strategies that are required to ensure an asset meets its mission requirements in its operational environment in the most safe and cost effective manner.
Reliability Centered Maintenance
Figure out how to manage each Failure Mode

## Slide 97
Proactive Maintenance Plan
New/Modifications to Operating Procedures
Failure Finding tasks
Updates/Additions to Technical Publications
New/Modifications to Training Programs
Equipment Redesigns
Troubleshooting Procedures
Supply Changes
RCM Can Yield
Potential Products of an RCM Analysis

## Slide 98
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.
Falsely illuminates the LOW OIL LEVEL Light.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Apply the RCM Decision Diagram

## Slide 99
Falsely illuminates the LOW OIL LEVEL Light.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)
Incapable of visually alerting the driver in the event that the engine oil level decreases to the lower limit.
LOW OIL LEVEL LIGHT circuit fails open.
This Failure Mode only matters in the event that the engine oil level decreases beyond the lower limit. The driver is unaware of the low oil situation and continues to operate the vehicle. The oil level continues to drop. Engine components are not properly lubricated and start to wear abnormally. Eventually, engine oil pressure decreases and engine oil temperature increases. The OIL PRESSURE warning light and/or the CHECK ENGINE light illuminates on the dashboard. Driver must pull over and cannot get to the desired destination on time. It is likely that the driver can find a safe place to pull over and call a tow truck. However, worst case, driver must pull over on a busy highway or on a dark country road at night. The oil system is repaired, as required. Any secondary engine damage is repaired, as required. Worst case, engine must be replaced. Downtime to repair, 3 days to 1 month at a cost ranging from $1,000 to $8,000.
Apply the RCM Decision Diagram

## Slide 100
Failure Effect
This Failure Mode only matters in the event that the engine oil level decreases to the lower limit. The driver is unaware of the low oil situation and continues to operate the vehicle. The oil level continues to drop. Engine components are not properly lubricated and start to wear abnormally. Eventually, engine oil pressure decreases and engine oil temperature increases. The OIL PRESSURE warning light and/or the CHECK ENGINE light illuminates on the dashboard. Driver must pull over and cannot get to the desired destination on time. It is likely driver can find a safe place to pull over and call a tow truck. However, worst case, driver must pull over on a busy highway or on a dark country road at night. The oil system is repaired, as required. Any secondary engine damage is repaired, as required. Worst case, engine must be replaced. Downtime to repair, 3 days to 1 month at a cost ranging from $1,000 to $8,000.
Failure Mode
LOW OIL LEVEL LIGHT circuit fails open.
Apply the RCM Decision Diagram
X
X
X

## Slide 101
RCM Process
1. Functions
2. Functional Failures
3. Failure Modes
4. Failure Effects
5. Failure Consequences
6. Proactive Maintenance and Intervals
7. Default Strategies
Reliability Centered Maintenance
Steps 1-4: FMEA
Failure Modes and Effects Analysis
Steps 1-5: FMECA
Failure Modes, Effects,
and Criticality Analysis

## Slide 102
Augment Failure Data with a Facilitated Working Group
FACILITATOR
Maintainer
Systems Engineer
OEM
Planner
Operator
RCM Analysis Working Group
“Work of art watching alignment.”
Need the people managers say “I can’t afford to lose them for a week.”

## Slide 103: NancyRegan@RCMTrainingOnline.com
Thank You!
NancyReganRCM
RCM Training Online

## Slide 105
BACKUP SLIDES ONLY

## Slide 106
Failure Mode
Destination:
Failure Management Strategies
Proactive Maintenance
and
Default Strategies
A properly written Failure Mode puts you on the right road and sends you in the right direction.
GOAL: Proactive Maintenance Plan

## Slide 107
Diesel engine fails
Engine oil deteriorates due to normal use
Engine oil diminishes due to normal use
Cooling fan drive belt wears due to normal use
Starter motor fails
Change the engine oil every 6 months.
Check engine oil level prior to use. Replenish, as required.
Visually inspect cooling fan drive belt every 500 operating hours. Replace, as required.
No scheduled maintenance
What specifically causes the diesel engine to fail?
How detailed should Failure Modes be written?
GOAL:
Proactive Maintenance Plan

## Slide 108
How detailed should Failure Modes be written?
Starter motor fails
No scheduled maintenance
Electrical connections loosen
Armature insulation breaks down
Solenoid fails
Starter motor fails
Brushes wear
Coil burns out
…and so on…
Plunger sticks
GOAL:
Proactive Maintenance Plan
Too Much Detail

## Slide 109
Resistance to Failure
Time
F: Structure fails



P2: Crack detectable using radiographic x-ray

P1: Crack detectable using ultrasonic inspection


P3: Crack detectable using eddy current
P4: Crack detectable using dye penetrant

P5: Crack detectable with the human eye
Structure is new
P-F Interval
Condition Based Maintenance (CBM)
P-F Curve
There can be more than one Potential Failure Condition

## Slide 110
Resistance to Failure
Time
F2: Component fails



F1: More than 5 pits (corrosion control no possible; component must be replaced)

P: Corrosion is visually detectable
Component installed
P-F1 Interval
3 months
P-F2 Interval
2 years
Condition Based Maintenance (CBM)
P-F Curve
There can be more than one “Failure.”

## Slide 111
Proactive Maintenance
Preventive Maintenance
Wear-Out Region
Conditional Probability of Failure
Age
Useful Life
F:
P:
Resistance to Failure
Time


6 months

Condition Based Maintenance (CBM)
Scheduled Restoration
Scheduled Replacement
Visual evidence of wear on belt
New V-belt installed
Belt breaks
Constant Failure Probability
How QUICKLY Failure Occurs
P-F Interval:
P-F Curve

## Slide 112
Failure Mode | Function | Functional Failure | Failure Mode | Failure Effect
1A1 | 1. To provide compressed air that is oil free, <95F, at a minimum of 3,500 SCFM, 100 psig output pressure, with a minimum of 5 psig rise to surge to make up this compressor's portion of maintaining 10,500 SCFM and 90 psig header pressure to the plant. | A. Unable to provide compressed air. | 1. Main drive shaft (coupling the motor to the compressor) lubrication dissipates. | Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place.

## Slide 113
Main drive shaft lubrication dissipates
Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place at a cost of $200,000.

## Slide 114
Main drive shaft lubrication dissipates
Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place at a cost of $200,000.

## Slide 115
Main drive shaft lubrication dissipates
Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place at a cost of $200,000.

## Slide 116
Main drive shaft lubrication dissipates
Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place at a cost of $200,000.

## Slide 117
Main drive shaft lubrication dissipates
Over time, this causes metal to metal contact which causes abnormal wear on the coupling teeth. Eventually, vibration levels increase. May cause excessive stress on the shaft, motor bearing(s), and the bullgear bearings. Vibration levels increase and are indicated on the system tab of the graphic display. Eventually, vibration levels increase such that the high vibration alarm system (from any one of the stages) produces alarm text on the INFO tab of the graphic display and illuminates the TROUBLE INDICATION light. If the text and the light go unnoticed, eventually, the vibration in one or more of the stages increases such that the high vibration trip system produces alarm text on the INFO tab, shuts down the compressor motor, energizes the prelube pump, and illuminates the PRELUBE PUMP RUNNING light. (The TROUBLE INDICATION light remains illuminated.) The inlet valve closes, and the bypass valve opens unloading the compressor. The graphic display indicates that the compressor is down. Possible internal damage to the motor, shaft, and/or the bullgear bearing. This causes low instrument air to the plant. It takes 2 days to replace the coupling but it could take weeks if the motor, shaft, and/or bullgear are damaged. Production stops for up to 2 days while an alternate means of producing instrument air is put in place at a cost of $200,000.

## Slide 118
, as required.
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Engine oil system leaks.
To transport up to 5 adult passengers and 3 medium-size suitcases along paved roads and highways for up to 360 miles without stopping in climates that range from 0º to 115º F (-17º to 46º C) while protecting passengers from the elements.

## Slide 119
Failure Modes and Effects Analysis (FMEA)
Engine oil system leaks.
Without warning, the system develops a leak. The leak is visually detectable on the ground.) If the visual leak goes unnoticed, the oil quantity gradually decreases. The decrease in oil is indicated on the dipstick. If this goes unnoticed, eventually the engine oil drops to the point that the LOW OIL LEVEL Light illuminates. The driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil is low. The driver replenishes the oil and continues to the destination but with some delay. Most likely, the leak is small and the driver is able to reach the destination with minimal delay. However, worst case, the leak is so extensive that the driver cannot complete the journey. Driver is stuck on the side of the road waiting for a tow truck. Worst case, this is at night on the highway or on a two-lane, dark country road. Downtime to repair, up to two weeks, up to $2,000.

## Slide 120
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)
What is another Functional Failure?
?

## Slide 121
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Falsely illuminates the LOW OIL LEVEL Light.
To be capable of visually alerting the driver in the event that the engine oil level decreases to the lower limit. (LOW OIL LEVEL light)
Falsely illuminates the LOW OIL LEVEL Light.

## Slide 122
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Falsely illuminates the LOW OIL LEVEL Light.
Falsely illuminates the LOW OIL LEVEL Light.
?
What specifically causes it to falsely illuminate?

## Slide 123
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Falsely illuminates the LOW OIL LEVEL Light.
Falsely illuminates the LOW OIL LEVEL Light.
LOW OIL LEVEL Light circuit fails closed.

## Slide 124
Copyright © The Force, Inc. 2017-2023 All Rights Reserved
Failure Modes and Effects Analysis (FMEA)
Falsely illuminates the LOW OIL LEVEL Light.
Falsely illuminates the LOW OIL LEVEL Light.
LOW OIL LEVEL Light circuit fails closed.
While driving, the LOW OIL LEVEL Light illuminates. The driver thinks that there is a low oil situation. Driver pulls over at the nearest service station and checks the oil. The dipstick indicates that the engine oil level is normal. The time it takes to check the oil is minimal so the driver is able to arrive at the intended destination with minimal delay. Driver schedules the vehicle for service at the next available opportunity. Time to repair, up to one day.